## Slide 1
PRODUCTIVE FACADES:
POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS
Abel Tablada
Assist Prof.
National
University
Singapore
Renewable Resources and Architecture: M. ‘Ammar Bin Mohamad Malek, Ng Zhi Li Sean, Wang Yigeng, Tay Lee Kuan Roy, 2015

## Slide 2
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
2/50 I. Background

## Slide 3
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
3/50 I. Background

## Slide 4
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
Dec 2015 by Eugene Tay
http://www.greenfuture.sg/2015/12/16/the-paris-agreement-what-it-means-for-singapore-and-what-more-can-we-do/
4/50 I. Background

## Slide 5
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
Source: CO2 Emissions from Fuel Combustion - 2015 Highlights © OECD/International Energy Agency, 2015
5/50 I. Background

## Slide 6
https://www.mti.gov.sg/ResearchRoom/Documents/app.mti.gov.sg/data/pages/885/doc/NEPR%202007.pdf
Notes: The only thing should be grown is happiness and satisfaction with owns lives
The actual smartness would be to achieve happiness without growing economy and ecological footprint
Energy intensity is just a step towards it, but it may become a hypocrisy is while increasing energy intensity, the total C)2 emissios and ecological footprint also grow

## Slide 7
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
Dec 2015 by Eugene Tay
http://www.greenfuture.sg/2015/12/16/the-paris-agreement-what-it-means-for-singapore-and-what-more-can-we-do/
7/50 I. Background

## Slide 8
Singapore 12th (21st 2007)
China
73th
 | Population | Gha/capita | Equivalent land (km2) | Actual country area (km2) | Times country area
Singapore | 5,400,000 | 6.1 | 329,400 | 716 | 460.0
China | 1,366,000,000 | 2.1 | 28,686,000 | 9,706,961 | 3.0
http://awsassets.panda.org/
Living Planet Report 2014 WWF

## Slide 10
Singapore
http://data.footprintnetwork.org/countryMetrics.html?cn=49&yr=

## Slide 11
Sri Lanka
Georgia
Cuba
Singapore
http://data.footprintnetwork.org/countryMetrics.html?cn=49&yr=

## Slide 12
719.1 km2
7,697 inh/km2
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
11/50 I. Background

## Slide 13
Food import: 90%
Local farms:
8% of vegetables,
8% of fish and
26% of eggs.
Farming area: 675 ha
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
12/50 I. Background

## Slide 14
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
13/50 I. Background

## Slide 15
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
14/50 I. Background

## Slide 16
Ecocity World Summit, Melbourne July 2017. FROM PRODUCTIVE FACADES TO PRODUCTIVE CITIES. Dr Abel TABLADA. Dept. of Archit., School of Design and Envir., NUS
15/50 I. Background

## Slide 17
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
16/50 I. Background

## Slide 18: Justification
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
17/50 I. Background

## Slide 19
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
18/50 II. Productivity potential at urban level

## Slide 20
Point block
Slab block
Contemporary block
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
19/50 II. Productivity potential at urban level

## Slide 21
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
20/50 II. Productivity potential at urban level

## Slide 22
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
21/50 II. Productivity potential at urban level

## Slide 23
22/50 II. Productivity potential at urban level
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 24
Food self-sufficiency is achieved with PR ≤ 1.9 if a hybrid farming method is applied (conventional + vertical).
Energy self-sufficiency is achieved for building height (< 42 m, < 14 storeys, PR < 3) due to the maximum exposed area with PV per amount of residents.
23/50 II. Productivity potential at urban level
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 25
Food self-sufficiency is achieved with PR ≤ 1.9 if a hybrid farming method is applied (conventional + vertical).
Energy self-sufficiency is achieved for building height (< 42 m, < 14 storeys, PR < 3) due to the maximum exposed area with PV per amount of residents.
Sunlight availability is sufficient for food and energy harvesting on all façade orientations.
For current typical New Towns in Singapore, food and energy self-sufficiency could reach about 60% and 80% respectively.
24/50 II. Productivity potential at urban level
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 26
To make recommendations for three categories of envelope use based on facade sunlight distribution:
25/50 II. Productivity potential at urban level
  1) only BIPV,
  (2) combination of BIPV and farming
  (3) only farming or solar collectors.
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 27
Food thresholds
Daylight Autonomy (DA)
required sunlight (RS)
Optimal RS = 80% > 10klx
Minimum RS = 40% > 10klx
Energy thresholds
Incident irradiance
PV > 800 kWh/m2
Solar collector > 400 kWh/m2
26/50 II. Productivity potential at urban level
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 28: Results (Food)
No facade and typology achieve the threshold requirement (RS=80%). All facades and sensor positions achieve RS > 40%.
North and south facades show minor differences (N 1-4% higher than S).
Higher differences were obtained between E & W facades which are more sensitive to sensor height position
27/50 II. Productivity potential at urban level
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 29: Results (Energy)
N & S facades are only suitable on the top positions for the denser cases. It may allow the whole facade for the least dense morphologies (PR = 1.3).
All cases achieve higher values than 400 kWh/m2, hence suitable for the installation of solar collectors on those facade locations not suitable for PV panels.
28/50 II. Productivity potential at urban level
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 30: Recommendations and partial conclusions
There is high potential of food and energy harvesting on building facades in low latitudes.
However, only densities lower than PR=3 allow the incidence of irradiance values above the threshold for energy harvesting
Farming and solar collectors can be installed on all facades at any height.
  However, it is recommended to be installed only on those facade areas where PV panels are not feasible based on irradiance threshold.
PV panels on the top section of all facades and farming and solar collectors on the remaining sections.
Cases | Farming 2nd category | PV (>800kWh/m2) |  |  |  | Solar collector
 |  | N | S | E | W | 
P1 | 100% | 100% | 33% | 0% | 100% | 100%
P3 | 100% | 50% | 33% | 0% | 75% | 100%
P5 | 100% | 25% | 25% | 0% | 50% | 100%
S1 | 100% | 100% | 50% | 0% | 100% | 100%
S3 | 100% | 33% | 33% | 0% | 100% | 100%
S5 | 100% | 33% | 33% | 0% | 100% | 100%
C1 | 100% | 100% | 100% | 0% | 100% | 100%
C3 | 100% | 50% | 0% | 0% | 100% | 100%
C5 | 100% | 33% | 0% | 0% | 33% | 100%
29/50 II. Productivity potential at urban level
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 31
Research team
Director:
Prof. Stephen Lau
Abel Tablada,
Siu Kit Lau,
Chao Yuan and
Shinya Okuda
NUS-CDL Tropical Technologies (T2) Lab
Collaborators/ sponsors
Hugh Tan, Dept of Biological Sciences, NUS.
Thomas Reindl and Veronika Shabunko, Solar Energy Research Institute of Singapore (SERIS)
Vesna Kosoric, Huang Huajing and Ian Chaplin from Dept of Architecture, NUS.
City Development Limited
30/50 IV. Productive facades / Design development
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 32
31/50 IV. Productive facades / Design development
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 33
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
32/50 IV. Productive facades / Design development

## Slide 34
1. Initial definition of PSF components
Definition of PV system
Definition of Food Planters
2. Formulation of decision goal
3. Formulation of relevant design alternatives
Facade wall (N,S,E,W)
Facade with balcony (N,S,E,W)
Selected Design Alternative should balance: production output, costs, user comfort and aesthetics
4. Determination of relevant assessment criteria functions and weight coefficients
5. Assigning the criteria scores to design alternatives
Survey with experts and residents
Computer simulations
Calculations
Quantitative
Qualitative
6. Evaluation of SPF design alternatives and selection of the optimal SPF design alternative
Accepting one Design: proceed to step 7
7. Optimal PSF Design Alternative
Not accepting design: return to any previous step
Façade installation and monitoring
Definition of openings
MCDA method/VIKOR
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
33/50 IV. Productive facades / Design development

## Slide 35
1. Initial definition of PSF components
Definition of PV system
Definition of Food Planters
2. Formulation of decision goal
3. Formulation of relevant design alternatives
Facade wall (N,S,E,W)
Facade with balcony (N,S,E,W)
Selected Design Alternative should balance: production output, costs, user comfort and aesthetics
4. Determination of relevant assessment criteria functions and weight coefficients
5. Assigning the criteria scores to design alternatives
Survey with experts and residents
Computer simulations
Calculations
Quantitative
Qualitative
6. Evaluation of SPF design alternatives and selection of the optimal SPF design alternative
Accepting one Design: proceed to step 7
7. Optimal PSF Design Alternative
Not accepting design: return to any previous step
Façade installation and monitoring
Definition of openings
MCDA method/VIKOR
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
34/50 IV. Productive facades / Design development

## Slide 36
Design alternatives
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
35/50 IV. Productive facades / Design development

## Slide 37
1. Initial definition of PSF components
Definition of PV system
Definition of Food Planters
2. Formulation of decision goal
3. Formulation of relevant design alternatives
Facade wall (N,S,E,W)
Facade with balcony (N,S,E,W)
Selected Design Alternative should balance: production output, costs, user comfort and aesthetics
4. Determination of relevant assessment criteria functions and weight coefficients
5. Assigning the criteria scores to design alternatives
Survey with experts and residents
Computer simulations
Calculations
Quantitative
Qualitative
6. Evaluation of SPF design alternatives and selection of the optimal SPF design alternative
Accepting one Design: proceed to step 7
7. Optimal PSF Design Alternative
Not accepting design: return to any previous step
Façade installation and monitoring
Definition of openings
MCDA method/VIKOR
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
36/50 IV. Productive facades / Design development

## Slide 38
Defining assessment criteria for façade optimization through the multiple criteria decision analysis (MCDA)
The VIKOR method relies on the weight coefficients of the criteria functions to model the preferred structure of a design strategy.
The MCDA VIKOR method is applied in order to provide a comprehensive evaluation and selection of the optimal design alternatives.
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
37/50 IV. Productive facades / Design development

## Slide 39
1. Initial definition of PSF components
Definition of PV system
Definition of Food Planters
2. Formulation of decision goal
3. Formulation of relevant design alternatives
Facade wall (N,S,E,W)
Facade with balcony (N,S,E,W)
Selected Design Alternative should balance: production output, costs, user comfort and aesthetics
4. Determination of relevant assessment criteria functions and weight coefficients
5. Assigning the criteria scores to design alternatives
Survey with experts and residents
Computer simulations
Calculations
Quantitative
Qualitative
6. Evaluation of SPF design alternatives and selection of the optimal SPF design alternative
Accepting one Design: proceed to step 7
7. Optimal PSF Design Alternative
Not accepting design: return to any previous step
Façade installation and monitoring
Definition of openings
MCDA method/VIKOR
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
38/50 IV. Productive facades / Design development

## Slide 40
Image of the Rhino model and the Grasshopper / Ladybug algorithm for the parametric calculation of building performance indicators and sunlight access.
Parametric simulation
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
39/50 IV. Productive facades / Design development

## Slide 41
Design variants
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
40/50 IV. Productive facades / Design development

## Slide 42
Design variants (total 12,180)
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
41/50 IV. Productive facades / Design development

## Slide 43
Example: Test-run of the simulation
Tilt angle
15/30/45
Protection angle
10/20/30
Start PV shading
Top facade/planter
Planter
configuration
3
3
2
13
x
x
x
234 Cases
42/50 IV. Productive facades / Design development
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 44
Simulation results
Best case
Prot. angle (20°) Tilt angle (30°)
Start shading (planter) Planter type (a10)
Second best case
Prot. angle (10°) Tilt angle (45°)
Start shading (top fac.) Planter type (a6)
43/50 IV. Productive facades / Design development
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 45
44/50 IV. Productive facades / Design development
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
Simulation results

## Slide 46
Extract of the survey to be conducted to residents of HDB buildings in order to obtain some of the criteria functions related to acceptance, accessibility and aesthetics.
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
45/50 IV. Productive facades / Design development
Survey to residents and experts

## Slide 47
1. Initial definition of PSF components
Definition of PV system
Definition of Food Planters
2. Formulation of decision goal
3. Formulation of relevant design alternatives
Facade wall (N,S,E,W)
Facade with balcony (N,S,E,W)
Selected Design Alternative should balance: production output, costs, user comfort and aesthetics
4. Determination of relevant assessment criteria functions and weight coefficients
5. Assigning the criteria scores to design alternatives
Survey with experts and residents
Computer simulations
Calculations
Quantitative
Qualitative
6. Evaluation of SPF design alternatives and selection of the optimal SPF design alternative
Accepting one Design: proceed to step 7
7. Optimal PSF Design Alternative
Not accepting design: return to any previous step
Façade installation and monitoring
Definition of openings
MCDA method/VIKOR
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
43/50 IV. Productive facades / Design development
Notes: The objective of the study we are presenting today is to develop…. For each façade orientation two types of facades are going to be tested, façade wall and with balcony or corridor.

## Slide 48
VIKOR: multiple criteria decision analysis (MCDA)
47/50 IV. Productive facades / Design development
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS

## Slide 49
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
48/50 IV. Productive facades / Design development

## Slide 50
1. Initial definition of PSF components
Definition of PV system
Definition of Food Planters
2. Formulation of decision goal
3. Formulation of relevant design alternatives
Facade wall (N,S,E,W)
Facade with balcony (N,S,E,W)
Selected Design Alternative should balance: production output, costs, user comfort and aesthetics
4. Determination of relevant assessment criteria functions and weight coefficients
5. Assigning the criteria scores to design alternatives
Survey with experts and residents
Computer simulations
Calculations
Quantitative
Qualitative
6. Evaluation of SPF design alternatives and selection of the optimal SPF design alternative
Accepting one Design: proceed to step 7
7. Optimal PSF Design Alternative
Not accepting design: return to any previous step
Façade installation and monitoring
Definition of openings
MCDA method/VIKOR
1st Int Conf on Smart Grid Technologies, Singapore Sept 2017. PRODUCTIVE FACADES: POTENTIAL ENERGY AND FOOD HARVESTING IN SINGAPORE’S RESIDENTIAL BUILDINGS. Dr Abel TABLADA. Dept of Arch., SDE, NUS
49/50 IV. Productive facades / Design development

## Slide 51
Thank you very much
Questions and suggestions
E-mail: abel@nus.edu.sg
50/50 Experiment results: to be reported next time!