## Slide 1
Application of MLVA-15 genotyping for typing of Brucella abortus isolates from India
Dr. Gita Kumari

## Slide 2
Brucellosis is considered as the most wide spread zoonosis
in the world and a True zoonosis
Genus - Brucella - Gram negative bacteria
Bovine brucellosis - B. abortus
    most widespread form in Cattle
    economic impact on livestock industry due to
abortions, stillbirths, weight loss, decreased
milk production, hazard to human health
    barriers to international trade of animals and their products (Corbel, 2006)
Introduction
Control and Eradication of infection - continuous surveillance and
epidemiological trace-back

## Slide 3: Trace-back Analysis
Strain-specific identification is essential
to know the source of infection
Requires a suitable typing technique for identification at sub-species level

## Slide 4: Molecular typing of Brucella
Outer membrane protein typing | Species-specific polymorphisms
Insertion sequence based typing | Limited subspecies level diversity
Pulsed field gel electrophoresis | -do-
Amplified fragment length polymorphism | -do-
Random Amplified Polymorphic DNA analysis | Sensitive to environmental conditions
Repetitive sequences based typing approaches (ERIC-PCR, REP-PCR, BOX A1R-PCR, (GTG)5-PCR, etc.) | Sensitive to environmental conditions
Multilocus sequence-typing (MLST) | Global epidemiology of bacteria
Multilocus Variable-Number Tandem-Repeat Analysis (MLVA) | Local epidemiology and epidemiological trace-back in outbreak cases

## Slide 5
Tandemly repeated sequences observed throughout the prokaryotic and eukaryotic genomes in thousands of copies
(Bennett, 2000; van Belkum et al., 1999)
Minisatellites : repeat unit sizes of 9 bp or greater
Microsatellites : repeat unit sizes of up to 8 bp
(Vergnaud and Pourcel. 2006)
Combinations of minisatellite and microsatellite repeats in MLVA proven highly discriminatory in subtyping of monomorphic bacterial species, like Brucella
(Bricker et al., 2003; Whatmore et al., 2006; Le Fleche et al., 2006)
High-speed molecular clocks (van Belkum, 1999).
Multilocus Variable-Number Tandem-Repeat Analysis (MLVA)

## Slide 6: MLVA contd….
PCR-based
Multiple alleles can be present at a single locus
Size differences could be easily resolved by electrophoresis (Lindstedt , 2005; Vergnaud and Pourcel , 2006)
When multiple loci are analyzed, the resulting fingerprint can be highly discriminatory or even unique.
Use of multiple loci avoids dangers of incorrect conclusions being drawn from single loci
Data can be easily stored and compared between laboratories leading to the development of International databases accessible via the Internet.

## Slide 7
  Field isolates of B. abortus- 13
  Reference strains- 4
B. melitensis 16M- Standard strain
Sl. No. | Reference Strains | Species-biovar | Acc. No.
1 | 544 | B. abortus bv 1 | ATCC 23448/NCTC10093
2 | S19 | B. Abortus | NCTC8038
3 | S99 | B. abortus | 
4 | 1119-R | B. abortus | 
MATERIALS & METHODS

## Slide 8
Field Isolates Of Brucella abortus Used For The Present Study
S. N. | Sample No./ Strain | Species-biovar | Host | Occupation | Source of isolation | Year of isolation | Place
1 | 12/02_VPH | Brucella abortus |  |  |  | 2002 | 
2 | M06_VPH | Brucella abortus |  |  |  | 2006 | 
3 | 07/VPH | Brucella abortus | Bovine |  | Aborted fetus | 2006 | Kolkata
4 | 19/VPH | Brucella abortus | Bovine |  |  | 2007 | West Bengal
5 | 21/VPH | Brucella abortus | Bovine |  |  | 2007 | West Bengal
6 | 22/VPH | Brucella abortus | Bovine |  |  | 2007 | West Bengal
7 | 47a(8)/VPH | Brucella abortus | Cattle |  |  | 2008 | Bangalore
8 | 11/08_VPH | Brucella abortus |  |  |  | 2008 | 
9 | 60/VPH | Brucella abortus | Cattle |  | Aborted materials | 2009 | CADRAD
10 | 61/VPH | Brucella abortus | Cattle |  | Aborted materials | 2009 | CADRAD
11 | 75/VPH | Brucella abortus | Bovine |  | Fetus | 2010 | Mizoram
12 | 76/VPH | Brucella abortus | Man | Butcher | Blood | 2010 | Maharashtra
13 | BAB_VPH | Brucella abortus |  |  |  |  | 

## Slide 9
Reaction mixture |  | Cycle condition | 
10X PCR buffer | 2.5 µl | Initial denaturation | 94oC for 5 min
dNTP | 2.5 µl(2mM each) | Denaturation | 94oC for 45 s
MgCl2 | 2.5 µl(2.5 mM) | Annealing | 55oC for 45 s
Forward primer | 1 µl (10 pmol/µl) | Extension | 72oC for 1 min
Reverse primer | 1 µl(10 pmol/µl) | Final extension | 72oC for5 min
Taq DNA polymerase | 0.2 µl |  | 
 | (1 unit) | Cycles | 30
Genomic DNA | 3 µl |  | 
NFW | 12.8 µl | Amplicon size: 410 bp | 
Total Volume | 25 µl |  | 
410bp
M 1 2 3 4 5 6
All the isolates were checked for purity & biochemical characteristics along with genus specific PCR (16S -23S r-RNA spacer gene) before use in the study
 | Name | Forward Primer (5'-3') | Reverse Primer (5'-3') | References
Genus specific PCR | 16S-23S r-RNA spacer genes | AAC ATA GAT CGC AGG CCA GTC AGC | TGC CAA TAT CCG TCT CAA GAC CAA | Kumar (2007)

## Slide 10
 | Name | Forward Primer (5'-3') | Reverse Primer (5'-3') | References
 | Panel 1 | Minisatellite Loci |  | 
 | Bruce 6 | ATG GGA TGT GGT AGG GTA ATC G | GCG TGA CAA TCG ACT TTT TGT C | 
 | Bruce 8 | ATT ATT CGC AGG CTC GTG ATT C | ACA GAA GGT TTT CCA GCT CGT C | 
 | Bruce 11 | CTG TTG ATC TGA CCT TGC AAC C | CCA GAC AAC AAC CTA CGT CCT G | 
 | Bruce 12 | CGG TAA ATC AAT TGT CCC ATG A | GCC CAA GTT CAA CAG GAG TTT C | 
 | Bruce 42 | CAT CGC CTC AAC TAT ACC GTC A | ACC GCA AAA TTT ACG CAT CG | 
 | Bruce 43 | TCT CAA GCC CGA TAT GGA GAA T | TAT TTT CCG CCT GCC CAT AAA C | 
MLVA-15 | Bruce 45 | ATC CTT GCC TCT CCC TAC CAG | CGG GTA AAT ATC AAT GGC TTG G | Le Fleche
 | Bruce 55 | TCA GGC TGT TTC GTC ATG TCT T | AAT CTG GCG TTC GAG TTG TTC T | et al.
 | Panel 2 | Microsatellite Loci |  | (2006)
 | Bruce 4 | CTG ACG AAG GGA AGG CAA TAA G | CGA TCT GGA GAT TAT CGG GAA G | 
 | Bruce 7 | GCT GAC GGG GAA GAA CAT CTA T | ACC CTT TTT CAG TCA AGG CAA A | 
 | Bruce 9 | GCG GAT TCG TTC TTC AGT TAT C | GGG AGT ATG TTT TGG TTG TAC ATA G | 
 | Bruce 16 | ACG GGA GTT TTT GTT GCT CAA T | GGC CAT GTT TCC GTT GAT TTA T | 
 | Bruce 18 | TAT GTT AGG GCA ATA GGG CAG T | GAT GGT TGA GAG CAT TGT GAA G | 
 | Bruce 21 | CTC ATG CGC AAC CAA AAC A | GAT TCG TGG TCG ATA ATC TCA TT | 
 | Bruce 30 | TGA CCG CAA AAC CAT ATC CTT C | TATGTGCAGAGCTTCATGTTCG | 
Oligonucleotide Primers used for MLVA Typing

## Slide 11
Sr. No. | Bruce | NFDW | Glycerol (10%) | 10x PCR Buffer | 2 mM dNTP Mix | MgCl2 (25mM) | Taq DNA Polymerase (5U/µl ) | Forward Primer (10pm) | Reverse Primer (10pm) | Genomic DNA | Total Reaction Volume
1 | 06 | 8.8 µl | 2.5µl | 2.5 µl (Final conc. of 1X) | 1.5 µl (Final conc. of 120µM of each) | 1.5 µl (1.5mM) | 0.2 µl (Final conc. 1U) | 1 µl (Final conc. of 10pM) | 1 µl (Final conc. of 10pM) | 4 µl | 25 µl
2 | 08 | 13.3 µl |  |  |  |  |  |  |  |  | 
3 | 11 | 13.3 µl |  |  |  |  |  |  |  |  | 
4 | 12 | 13.3 µl |  |  |  |  |  |  |  |  | 
5 | 42 | 8.8 µl | 2.5µl |  |  |  |  |  |  |  | 
6 | 43 | 13.3 µl |  |  |  |  |  |  |  |  | 
7 | 45 | 13.3 µl |  |  |  |  |  |  |  |  | 
8 | 55 | 13.3 µl |  |  |  |  |  |  |  |  | 
9 | 04 | 13.3 µl |  |  |  |  |  |  |  |  | 
10 | 07 | 13.3 µl |  |  |  |  |  |  |  |  | 
11 | 09 | 13.3 µl |  |  |  |  |  |  |  |  | 
12 | 16 | 13.3 µl |  |  |  |  |  |  |  |  | 
13 | 18 | 13.3 µl |  |  |  |  |  |  |  |  | 
14 | 21 | 13.3 µl |  |  |  |  |  |  |  |  | 
15 | 30 | 13.3 µl |  |  |  |  |  |  |  |  | 
PCR reaction mix for 15 VNTR loci
    MLVA-15 Genotyping

## Slide 12: Amplification conditions for the 15 VNTR loci
Sr. No. | Bruce | STEP1 Initial Denaturation | STEP2 Denaturation | STEP3 Annealing | STEP4 Extension | STEP5 Repeat (Steps 2 to 4) | Final Extension | Hold
1 | 06 | 96°C for 5 min | 96°C for 30 sec | 62⁰C for 30 sec | 70⁰C for 1 min | 30 cycles | 70°C for 5 min | 4°C for Infinite
2 | 08 |  |  | 60⁰C for 30 sec |  |  |  | 
3 | 11 |  |  |  |  |  |  | 
4 | 12 |  |  |  |  |  |  | 
5 | 42 |  |  |  |  |  |  | 
6 | 43 |  |  |  |  |  |  | 
7 | 45 |  |  | 61⁰C for 30 sec |  |  |  | 
8 | 55 |  |  |  |  |  |  | 
9 | 04 |  |  | 55⁰C for 30 sec |  | 34 cycles |  | 
10 | 07 |  |  | 61⁰C for 30 sec |  | 30 cycles |  | 
11 | 09 |  |  | 55⁰C for 30 sec |  | 34 cycles |  | 
12 | 16 |  |  |  |  |  |  | 
13 | 18 |  |  |  |  |  |  | 
14 | 21 |  |  | 60⁰C for 30 sec |  | 30 cycles |  | 
15 | 30 |  |  | 55⁰C for 30 sec |  | 34 cycles |  | 

## Slide 13: Analysis of PCR Products
Done by Agarose Gel Electrophoresis
Minisatellites (Panel 1 Loci)
  2% (w/v) Agarose gel
  100bp and 50bp DNA ladder
  constant 80V for 3 to 4 h depending on the particular VNTR loci.
Microsatellites (Panel 2 Loci)
  4% (w/v) High Resolution Agarose gel
  20bp DNA ladder
  constant 80V for 6 h

## Slide 14: Amplicon size determination and calculation of number of repeat at particular loci
Comparing with standard strain’s amplicon size (B. melitensis 16M, ATCC 23456)
100bp DNA ladder
50bp DNA ladder
20bp DNA ladder
Respective number of repeat at particular loci with the help of VNTR allelic Table

## Slide 16
Sl. No. | Locus | VNTR Name | PCR product size(bp) | Tandem repeats (bp) | Unit size
 | Panel 1 |  |  |  | 
1 | Bruce06 | BRU1322_134bp_408bp_3u | 408 | 134 | 3
2 | Bruce08 | BRU1134_18bp_348bp_4u | 348 | 18 | 4
3 | Bruce11 | BRU211_63bp_257bp_2u | 257 | 63 | 2
4 | Bruce12 | BRU73_15bp_392bp_13u | 392 | 15 | 13
5 | Bruce42 | BRU424_125bp_539bp_4u | 539 | 125 | 4
6 | Bruce43 | BRU379_12bp_182bp_2u | 182 | 12 | 2
7 | Bruce45 | BRU233_18bp_151bp_3u | 151 | 18 | 3
8 | Bruce55 | BRU2066_40bp_273bp_3u | 273 | 40 | 3
 | Panel 2 |  |  |  | 
9 | Bruce04 | BRU1543_8bp_152bp_2u | 152 | 8 | 2
10 | Bruce07 | BRU1250_8bp_158bp_5u | 158 | 8 | 5
11 | Bruce09 | BRU588_8bp_156bp_7u | 156 | 8 | 7
12 | Bruce16 | BRU548_8bp_152bp_3u | 152 | 8 | 3
13 | Bruce18 | BRU339_8bp_146bp_5u | 146 | 8 | 5
14 | Bruce21 | BRU329_8bp_148bp_6u | 148 | 8 | 6
15 | Bruce30 | BRU1505_8bp_151bp_6u | 151 | 8 | 6
Repeat number present at each locus in standard strain (Brucella melitensis 16M, ATCC 23456)

## Slide 17: Analysis of MLVA-15 genotyping
START (Sequence Type Analysis and Recombinational Test) software, version 1.0.5 (Jolley et al., 2001)
  Allelic profile frequencies
  Allele frequencies
  Phylogenetic tree by UPGMA method
Hunter-Gaston diversity index (HGDI)
  Measure of the variability of the TRs copy number at each locus.
  V-DICE (VNTR diversity and confidence extractor) (http://www.hpa.org.uk)

## Slide 18
S.N. | B. abortus strains | 6 | 8 | 11 | 12 | 42 | 43 | 45 | 55 | 4 | 7 | 9 | 16 | 18 | 21 | 30
1 | 12/02_VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 4 | 4 | 3 | 3 | 6 | 8 | 6
2 | M06_VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 5 | 3 | 3 | 7 | 8 | 6
3 | 07/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 6 | 8 | 8
4 | 19/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 6 | 8 | 7
5 | 21/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 6 | 8 | 7
6 | 22/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 7 | 8 | 7
7 | 47a(8)/VPH | 4 | 5 | 4 | 13 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 7 | 8 | 5
8 | 11/08_VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 6 | 8 | 6
9 | 60/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 6 | 8 | 6
10 | 61/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 6 | 8 | 6
11 | 75/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 4 | 3 | 3 | 6 | 8 | 5
12 | 76/VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 5 | 3 | 3 | 6 | 8 | 5
13 | BAB_VPH | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 6 | 3 | 3 | 6 | 8 | 5
14 | Ref 544 | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 5 | 3 | 4 | 6 | 8 | 5
15 | Ref S 19 | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 6 | 3 | 3 | 6 | 8 | 5
16 | Ref S99 | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 5 | 3 | 4 | 6 | 8 | 6
17 | Ref 1119-R | 4 | 5 | 4 | 12 | 2 | 2 | 3 | 3 | 3 | 6 | 4 | 3 | 6 | 8 | 5
Number of tandem repeats determined at each locus for
B. abortus strains
results

## Slide 19
Genotype | Profile ( Bruce 06, 08, 11, 12, 42, 43, 45, 55, 04, 07, 09, 16, 18, 21, 30) | Frequency | % of dataset
A1 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 4, 3, 3, 6, 8, 6 | 3 | 17.65
A2 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 4, 3, 3, 6, 8, 7 | 2 | 11.76
A3 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 6, 3, 3, 6, 8, 5 | 2 | 11.76
A4 | 4, 5, 4, 12, 2, 2, 3, 3, 4, 4, 3, 3, 6, 8, 6 | 1 | 5.88
A5 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 5, 3, 3, 7, 8, 6 | 1 | 5.88
A6 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 4, 3, 3, 6, 8, 8 | 1 | 5.88
A7 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 4, 3, 3, 7, 8, 7 | 1 | 5.88
A8 | 4, 5, 4, 13, 2, 2, 3, 3, 3, 4, 3, 3, 7, 8, 5 | 1 | 5.88
A9 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 4, 3, 3, 6, 8, 5 | 1 | 5.88
A10 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 5, 3, 3, 6, 8, 5 | 1 | 5.88
A11 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 5, 3, 4, 6, 8, 5 | 1 | 5.88
A12 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 5, 3, 4, 6, 8, 6 | 1 | 5.88
A13 | 4, 5, 4, 12, 2, 2, 3, 3, 3, 6, 4, 3, 6, 8, 5 | 1 | 5.88
Allelic profile frequencies of B. abortus
13 different profile(s) in dataset (displayed in descending order of frequency)

## Slide 20
Allelic frequencies and Allelic Diversity of B. abortus
Allele | 6 | 8 | 11 | 12 | 42 | 43 | 45 | 55 | 4 | 7 | 9 | 16 | 18 | 21 | 30
1 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | -
2 | - | - | - | - | 17 | 17 | - | - | - | - | - | - | - | - | -
3 | - | - | - | - | - | - | 17 | 17 | 16 | - | 16 | 15 | - | - | -
4 | 17 | - | 17 | - | - | - | - | - | 1 | 10 | 1 | 2 | - | - | -
5 | - | 17 | - | - | - | - | - | - | - | 4 | - | - | - | - | 7
6 | - | - | - | - | - | - | - | - | - | 3 | - | - | 14 | - | 6
7 | - | - | - | - | - | - | - | - | - | - | - | - | 3 | - | 3
8 | - | - | - | - | - | - | - | - | - | - | - | - | - | 17 | 1
9 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | -
10 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | -
11 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | -
12 | - | - | - | 16 | - | - | - | - | - | - | - | - | - | - | -
13 | - | - | - | 1 | - | - | - | - | - | - | - | - | - | - | -
Total | 1 | 1 | 1 | 2 | 1 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 2 | 1 | 4
Allelic Diversity | 0.000 | 0.000 | 0.000 | 0.118 | 0.000 | 0.000 | 0.000 | 0.000 | 0.118 | 0.603 | 0.118 | 0.221 | 0.309 | 0.000 | 0.713

## Slide 21
Phylogenetic tree constructed from MLVA-15 fingerprinting of B.abortus strains using UPGMA
13 types observed out of 17 strains
Isolates that clustered together had same place and year of isolation

## Slide 22
Dendrogram showing comparison of Indian Brucella abortus strains with the foreign Brucella abortus strains (http://mlva.u-psud.fr)
Same allelic profile of
B. abortus, 76/VPH (Maharashtra ) and BCCN V1 B. abortus biovar 1 United states)
B. abortus , 75/VPH (Mizoram) and BCCN 95-55 B.abortus biovar 1 (Costa Rica)

## Slide 23: Summary and conclusion
17 Brucella abortus strains (13 field isolates & 4 reference strains) were used in MLVA-15 genotyping
MLVA-15 genotyping clearly discriminated Indian field isolates of Brucella abortus producing 13 genotypes
The isolates that grouped together were of same source
  So, MLVA-15 genotyping sufficiently discriminated Indian field isolates of Brucella abortus.
  Specific grouping was also observed according to epidemiological data/source of infection

## Slide 24
Thanks