## Slide 1
Q. Lu1, R.A. de Toledo 1, F. Xie1, J. Li1,2, H. Shim1
1Department of Civil and Environmental Engineering, Faculty of Science and Technology, University of Macau, Macau SAR, China.
2 College of Natural Resources and Environmental Science, South China Agricultural University, Guangzhou, China.
Enhanced removal of BTEX/TCE/cis-DCE mixture using waste scrap tires immobilized with indigenous Pseudomonas sp.

## Slide 2
INTRODUCTION
Waste Tires Recycling
3 billion car and truck tires are discarded
Chart: 
| Fuel | Recycled or used in civil engineering projects | Converted into ground rubber and recycled into products | Converted into ground rubber and used as asphalt | Exported | Recycled into cut/stamped/punched products | Used in agricultural and miscellaneous uses
 | 44.7 | 19.4 | 7.8 | 4.3 | 3.1 | 2 | 1.7

## Slide 3
INTRODUCTION
Waste tires: sorption phase
2,4-dichlorophenol (83% removal)
4-nitrophenol (~100% removal)
Two-Phase Partitioning Bioreactor (TPPB) with 10% and 15% (v/v) tires*
* Tomeia MC, Angeluccia DM, Daugulis AJ (2014) Environ Technol 35:75-81
Chart: Tire component
| Rubber | Carbon black | Metal | Additives | Textile | Sulphur | Zinc oxide
 | 47 | 21.5 | 16.5 | 7.5 | 5.5 | 1 | 1
Car tire composition

## Slide 4
BACKGROUND
BTEX: Benzene, Toluene, Ethylbenzene, and Xylenes (ortho-, meta-, and para-)
    Major monoaromatic components in petroleum products
    Industrial solvents and equipment cleansing
    Among priority pollutants (US EPA)
    Benzene (carcinogen)
Spills from leaking oil tanks
Common source of BTEX contamination:

## Slide 5
BACKGROUND
Chlorinated Aliphatic Hydrocarbons (CAHs):
      Most widespread contaminants in subsurface
      Cleaning and degreasing solvents
Perchloroethylene (PCE), trichloroethylene (TCE), dichloroethylenes (DCEs), vinyl chloride (VC).
      TCE: the most frequently found contaminant in groundwater (US)
      Carcinogen

## Slide 6
Microbial degradation of CAHs:
anaerobic reductive dechlorination (Dehalococcoides)
6
Aerobic cometabolism
BACKGROUND

## Slide 7
BACKGROUND
BTEX and CAHs:
BTEX/CAHs mixture: biological
Soil
Water
Hybrid technology (biological + physical)
Further improvements: CAHs removal
Biological
Chemical
Physical
Cost-effective
Environmental-friendly
Contaminant mineralization

## Slide 8
To remove BTEX/cis-DCE/TCE mixture from artificially contaminated water using indigenous bacterial isolate, Pseudomonas plecoglossicida
To utilize scrap tires (waste) for hybrid/enhanced removal of mixture; physical/adsorption and biological/immobilization
OBJECTIVES

## Slide 9
Experimental setup
Contaminants concentrations:
BTEX (300 mg L-1): based on mass fractions in crude oil (benzene: toluene: ethylbenzene: o-xylene: m-xylene: p-xylene at 22.7%: 48.3%: 4.6%: 6.3%: 6.9%: 11.1%)
TCE (10 mg L-1) and cis-DCE (5 mg L-1)
MATERIALS AND METHODS
Serum bottle: MSM (mineral salts medium) solution (45 mL)
Contaminants
Inoculum (5 mL)
Scrap tires (1.3, 2.8, and 4.0 g).
Incubation: 150 rpm , 25°C, pH 7, 5 days.
9
Microcosms: suspended and immobilized systems

## Slide 10
Adsorption kinetics of BTEX onto tire surface
Sorption capacity (qe) of adsorbent calculated by:
C0 and Ce, initial and equilibrium concentrations (mg L-1);
m, mass of adsorbent (g);
V, solution volume (L).
MATERIALS AND METHODS
Concentrations used in bioremoval experiments
BTEX: 300 mg L-1
TCE: 10 mg L-1
cis-DCE: 5 mg L-1
Sampling: 0.25, 0.5, 1, 1.5, 24, 48, and 72 h
10

## Slide 11
MATERIALS AND METHODS
Scrap tires
Bridgestone (BATTLAX BT-39 tubeless)
Cut into small pieces (0.2 cm x 0.2 cm x 0.2 cm)
Weighed and autoclaved for 1 h (121°C, 103.5 kPa)
Microbial culture
Pure culture of Pseudomonas plecoglossicida
Isolated from a heavily petroleum-contaminated site (Xiamen, China)

## Slide 12
Adsorption studies
Adsorption kinetics of individual BTEX compounds (total concentration, 300 mg L-1), TCE (10 mg L-1), and cis-DCE (5 mg L-1). Mass of tire: 26 mg/mg.
RESULTS
12

## Slide 13
RESULTS
Adsorption studies (each BTEX, 100 mg L-1)
Adsorption kinetics of individual BTEX (100 mg L-1).
Mass of tire: 26 mg/mg.
(b) Removal efficiencies for individual BTEX in multi and single solution.
(a)
(b)
  Octanol-water partitioning coefficient (Kow)
  3.15 (xylenes and ethylbenzene)
  2.73 (toluene)
  2.13 (benzene)

## Slide 14
Bioremoval by immobilized (attached) microorganisms
RESULTS
Removal efficiency (%) for each compound in mixture under different conditions
after 5 days of incubation
T: Tire in the absence of microorganisms
MT: Tire with microorganisms
BM: Microorganisms only
1.5, 3.0, 4.0: Different mass of tires
Surface area (cm2) | Benzene | Toluene | Ethylbenzene | m,p-Xylene | o-Xylene | cis-DCE | TCE
T1.57.2 | 70.6±3.2 | 75.4±2.3 | 92.8±1.4 | 92.0±1.1 | 92.1±0.9 | 47.0±3.4 | 54.1±3.4
T3.014.4 | 84.2±2.1 | 82.4±1.2 | 95.6±1.8 | 96.8±0.4 | 97.2±0.3 | 53.7±3.1 | 64.0±2.8
T4.0 19.2 | 88.6±1.3 | 82.8±2.2 | 98.3±0.3 | 97.6±0.2 | 97.9±0.4 | 64.6±2.2 | 62.5±2.5
MT1.57.2 | 99.6±0.2 | 100 | 95.5±0.7 | 96.5±0.3 | 98.2±0.2 | 60.0±1.7 | 70.3±1.7
MT3.014.4 | 100 | 100 | 97.8±0.4 | 96.3±0.4 | 98.5±0.3 | 60.8±2.4 | 71.6±2.5
MT4.019.2 | 100 | 100 | 100 | 96.8±0.3 | 99.0±0.1 | 61.6±0.9 | 73.0±2.8
BM | 99.5±0.2 | 97.6±0.1 | 88.0±0.4 | 64.5±3.3 | 56.0±2.7 | 20.4±1.2 | 36.3±2.0

## Slide 15
==
Contact angle (93.4±4.1°)
RESULTS
Measurement of contact angle for tire sample over time. Drop volume: 5 L. a) Water drop before experiment; b) Water drop after experiment.
a
b
15

## Slide 16
CONCLUSION
Scrap tire (waste) is considered a good candidate to enhance removal of VOCs such as BTEX, cis-DCE, and TCE from liquid phase, due to remarkable adsorption properties as well as capability to immobilize (attach/entrap) microorganisms.
Further studies are in progress to evaluate whether the immobilized microorganism possess the same initial removal efficiency after the reutilization cycles, including whether higher concentrations of contaminants can also be applied.

## Slide 17
ACKNOWLEDGEMENTS
University of Macau Multi-Year Research Grant (MYRG2014-00112-FST)
Macau Science and Technology Development Fund (FDCT/063/2013/A2)
Mr. Lu, PhD student; Dr. Li, SCAU/China; Mr. Xie, MS student