## Slide 1: A PRESENTATION ON SEA-LEVEL RISE AND COASTAL SUBMERGENCE ALONG THE SOUTH –EAST COAST OF NIGERIA
BY SAVIOUR P. UDO-AKUAIBIT INSTITUTE OF NATURAL RESOURCES, ENVIRONMENT AND SUSTAINABLE DEVELOPMENT, UNIVERSITY OF PORT HARCOURT, RIVERS STATE, NIGERIA.
at the 2nd International Conference on Oceanography, Las Vegas, USA., July 21-23, 2014.

## Slide 2: OUTLINE
INTRODUCTON
STUDY AREA&TECHNIQUES
RESULTS/DISCUSSION
SUMMARY
CONCLUSION

## Slide 3: INTRODUCTION
Coastal submergence and shoreline retreat are global problems which can be attributed to sea- level rise and climate change. These constitute a serious threat to shoreline management in the Niger Delta.
This study is therefore aimed at analyzing shoreline recession as a result of sea level rise and also examines the impact on the strand coast, south eastern Nigeria.

## Slide 4: STUDY AREA &TECHNIQUES
Period Sept.28- October 6, 2013
Shoreline Mapping with GPS and camera.
Wave breaker parameters
Beach profile surveys

## Slide 5
The 2002 And 2013 Editions Of The Shoreline Maps Of The Study Area
Notes: 2002 and 2013 editions of the shoreline maps of the study area

## Slide 6: STUDY AREA
Plate 1: Aerial photo of Qua-Iboe Estuary in 2002
Notes: Plate 1 Aerial photo of Qua-Iboe Estuary in 2002

## Slide 7
Plate 2: Aerial photo of Qua-Iboe estuary showing areas of severe erosion in 2002
Notes: Plate 2: Aerial photo of Qua-Iboe estuary in 2002 showing areas of severe erosion

## Slide 8: RESULT-ESTUARY: Current Velocities
Chart: Estuarine current velocity-Updrift
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Neap Tide | -13 | -15 | -9 | 0 | 10 | 10 | 15 | 10 | 19 | 30 | 17 | 14 | 13 | -39 | -61 | -83 | -100 | -105 | -111
Mean Tide | -56 | -75 | -56 | -43 | -29 | -16 | -10 | -8 | -5 | 0 | 14 | 14 | 16 | 35 | 46 | 72 | 75 | 113 | 24 | 8 | -6
Spring Tide | -71 | -77 | -100 | -125 | -111 | -71 | 0 | -77 | -46 | -36 | -7 | 19 | 43 | 67 | 83 | 29 | 45 | 27 | 35 | 63 | 39 | 32 | 22
Chart: Average Flow Velocity:Estuary- Updrift
| Neap Tide | Mean Tide | Spring Tide | Neap Tide | Mean Tide | Spring Tide | Flood Tide | Ebb tide
 | 15.33 | 40.1 | 46.33 | 55.22 | 30.1 | 72.15
Chart: Estuarine Current: Downdrift
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Neap Tide | -31 | -20 | -16 | -16 | -14 | -11 | -7 | 0 | 9 | 11 | 13 | 17 | 32 | 53 | 13 | 21 | 25 | -35 | -38
Mean Tide | 37 | 49 | 0 | 45 | 49 | 35 | 26 | 27 | 21 | -26 | -27 | -40 | -29 | -31
Spring Tide | -47 | -41 | -74 | -74 | -77 | -58 | -50 | -26 | -17 | 0 | 32 | 25 | 55 | 72 | 69 | 98 | 107 | 61 | 59 | 43
Chart: Average Flow Velocity: Estuary-Downdrift
| Neap Tide | Mean Tide | Spring Tide | Neap Tide | Mean Tide | Spring Tide | Flood Tide(Northward) | Ebb Tide(Southward)
 | 24.22 | 34.29 | 60 | 20.89 | 36 | 56.63
Fig.4.Estuarine current velocity-Updrift
Fig.6.Average Flow Velocity:Estuary updrift
Fig.5.Estuarine current velocity:downdrift
Fig.7 Average Flow Velocity: Estuary Downdrift

## Slide 9: RESULT-SURF ZONE: Longshore Current
Chart: Fig. 8: Longshore current velocity:Updrift station 1
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Neap Tide | 22 | 35 | 29 | 0 | 36 | 41 | 46 | 56 | 67 | 76 | 8 | 10 | 0 | 8 | 11 | 11 | 9 | 14 | 17
Mean Tide | 59 | 67 | 80 | 62 | 89 | -100 | -125 | 125 | 83 | 101 | 52 | 40 | 31 | 54 | 113 | 72 | 36 | 21 | 0 | 29 | 20
Spring Tide | 40 | 53 | 71 | 30 | 20 | 16 | 18 | 0 | 11 | 13 | 14 | -41 | 18 | 53 | 63 | 36 | 30 | 22 | 40 | 56 | 0 | 0 | 7
Chart: Fig.10: Average Longshore Current Velocity: Updrift-Station 1
| Neap Tide | Mean Tide | Spring Tide | Neap Tide | Mean Tide | Spring Tide | East | West
 | 29.18 | 63.19 | 31.41 | 0 | 112.5 | 41
Chart: Fig. 9: Longshore current velocity:Downdrift station 1
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Neap Tide | 63 | 59 | 79 | 70 | -88 | -77 | -88 | -72 | -50 | 46 | 42 | 34 | -41 | 0 | 79 | 64 | -52 | -57 | -85
Mean Tide | -12 | -8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spring Tide | -14 | -24 | -17 | -25 | -13 | -9 | -11 | -13 | -13 | -12 | -14 | -25 | -33 | -50 | -20 | -33 | -17 | -17
Chart: Fig. 11: Average Longshore Current Velocity:Downdrift Staiton 1
| Neap Tide | Mean Tide | Spring Tide | Neap Tide | Mean Tide | Spring Tide | East | West
 | 57.7 | 0 | 0 | 64.29 | 10 | 20

## Slide 10: RESULT-SURF ZONE: UPDRIFT.ST.2 -WAVE PARAMETER
Chart: Fig 12: Wave Breaker height:Updrift
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Neap Tide | 7 | 5 | 10 | 10 | 10 | 8 | 7 | 13 | 26 | 22 | 15 | 13 | 18 | 21 | 10

Chart: Fig 13: Wave Breaker Height: Downdrift
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Neap Tide | 29 | 24 | 27 | 27 | 26 | 23 | 24 | 26 | 23 | 23 | 21 | 23 | 21 | 25 | 23 | 23 | 27 | 25
Mean tide | 31 | 30 | 40 | 39 | 44 | 36 | 47 | 50 | 54 | 60 | 37 | 36
SpringTide | 35 | 35 | 35 | 34 | 33 | 31 | 30 | 34 | 40 | 34 | 52 | 54 | 54 | 54 | 51 | 57 | 56 | 56 | 56
Plate 3.Wave breaker Height -Updrift
Plate 4: Wave breaker Height- Downdrift.

## Slide 11: RESULT-UPDRIFT:BEACH PROFILE
Chart: Beach Profile:Updrift -Station 1
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Neap Tide | 0 | -14 | 12 | 12 | 10 | 12 | 14 | 14 | 14 | 4 | -64 | -48 | -38 | -12
Mean Tide | 0 | -26 | 26 | 12 | 10 | 12 | 14 | 12 | 14 | 6 | -70 | -48 | -38 | -30 | -2 | 2
Spring Tide | 0 | -20 | 20 | 10 | 14 | 12 | 14 | 18 | 14 | -76 | -48 | -34 | -38 | -8 | 10 | 30 | 16 | -30 | -30
Chart: Beach Profile:Updrift-Station 2
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Neap Tide | 0 | 16 | 8 | -58 | -36 | -34 | -56
Mean Tide | 0 | 16 | 10 | -56 | -42 | -30 | -34 | -62 | -30 | 28 | 4 | 1 | -1 | -1 | -6 | -6 | -8
Spring Tide | 0 | 12 | 8 | -48 | -42 | -34 | -30 | -32 | -68 | -28 | 4 | 2 | -4 | -8 | -2 | -4 | -10 | -6 | -12 | -14
Fig.14.Beach Profile: Updrift-Station 1
Fig.15. Beach Profile: Updrift Station 2
Plate 5:Backshore - Updrift Station 1
Plate6: Foreshore –Updrift Station 2

## Slide 12: RESULT-DOWNDRIFT:BEACH PROFILE
Chart: Beach Profile:Downdrift-Station 1
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
Neap Tide | 0 | 12 | 6 | -64 | -60 | -48 | -52 | -60 | -52 | -46
Mean Tide | 0 | -52 | -34 | -30 | -24 | -18 | -12 | -6 | -4 | -4 | -8 | -14
Spring Tide | 0 | -28 | -56 | -32 | -20 | -14 | -10 | -8 | -8 | -10 | -6 | -8 | 16 | 22
Chart: Beach Profile:Downdrift-Station 2
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Neap Tide | 0 | 10 | 20 | 36 | 24 | -68 | -32 | -44 | -44 | -36 | -38
Mean Tide | 0 | 8 | 4 | -26 | -28 | -18 | -20 | -28 | -20 | -28 | -20 | -14 | -10 | -6 | -6 | -12
Spring Tide | 0 | 2 | -10 | -8 | -32 | -32 | -18 | -18 | -14 | -12 | -12 | -10 | -10 | -14 | -24
Fig.16.Beach Profile: Downdrift Station1
Fig17.Beach Profile: Downdrift-Station 2
Plate 7: Foreshore- Downdrift Station 1
Plate 8: Foreshore- Downdrift Station 2

## Slide 13: HYDRODYNAMICS-EBB PHASE
Plate 9. Offshore sand bar –Updrift.

## Slide 14: SHORELINE MANAGEMENT ISSUES
Plate 10 Stubb’s Creek sealed-up with sediment during storm surge in 2011
Plate 11: Foreshore trough at updrift beach
Plate 12: Eroded backshore at updrift beach
Plate 13: Beach Transportation-Updrift
Plate 13 shoreline retreat due to storm surge event at the updrift
Notes: Plate 13 shoreline retreat due to storm surge event at the updrift

## Slide 15: SHORELINE MANAGEMENT ISSUES
Plate 14:Former Itak Abasi primary School damaged by storm surge in 2011
Plate 15: Former Itak Abasi Health Centre damaged by storm surge in 2011
Plate 16: Ibeno beach resort
Plate17: sediment accretion at downdrift beach

## Slide 16: SUMMARY
This presentation has :
Noted shoreline retreat and coastal submergence around Qua-Iboe Estuary as impact of sea-level rise and climate change in Nigeria.
Considered integrated coastal zone management approach as essential in managing the shoreline retreat through intervention projects by both public and private sectors.
Considered regular beach nourishment as a proactive measure to prevent shoreline retreat

## Slide 17: CONCLUSION
In conclusion, the coastal submergence and shoreline retreat along the south east coast of Nigeria which is attributed to sea-level rise related storm surge can be considered as a signature of climate change in Nigeria. Therefore, more attentions should be given and concerted effort made by the government and private sectors to reduce any anthropogenic activity which accelerate climate change and sea-level rise.

## Slide 18: CONTRIBUTION TO KNOWLEDGE
The production of a recent shoreline map of the study area as a basis for assessment of sea-level rise along the strand coast of Akwa Ibom State, South-eastern Nigeria.

## Slide 19: THANK YOU FOR LISTENING