## Slide 1: Intelligent LED Brightness Control System Using Internet-of-Things Technology
July 20, 2015
Suk-Ju Kang
Intelligent Signal System Laboratory
Dong-A University

## Slide 2: Outline
Introduction
1st Proposed algorithm (Intelligent LED brightness control system)
  Algorithm description
  Simulation results
2nd Proposed algorithm (Automatic chlorophyll estimation algorithm)
  Algorithm description
  Simulation results
Summary

## Slide 3: Introduction
Internet of things (IoT)
  The connectivity among objects and humans is more and more important, and the key technology is the internet of things
  IoT uses various types of multiple sensors
    Light, humidity, temperature….
The Internet of Things(IoT)

## Slide 4: Introduction
Benefits of Internet of Things
  Information : Providing more information helps making better decisions
  Monitor : monitoring environmental conditions can help users
  Time : the amount of time saved because of IoT’s convenience
Monitoring System for user
Place information acquisition

## Slide 5: Introduction
Conventional home plant cultivation
  Many people have been cultivating vegetables at home to get vegetables
  In this way, people can easily get fresh vegetables
The old way home plant cultivation
The way cultivate lettuce

## Slide 6: Introduction
Limitation of conventional home plant cultivation
  To make an environment for home plant cultivation, the amount of sunshine and water are required
  Due to changing weather conditions, it is difficult to provide the amount of sunshine to plants
    Photosynthetic rate decreases in dark environment
Plant growth in different light conditions
Photosynthetic rate in different light intensity

## Slide 7: Introduction
There is a method to use the LED grow light for providing the amount of sunshine artificially
Advantages for the LED grow light
  Supplying light efficiently
  Saving electric energy
  Saving household budget
  Adding the beauty at home
Comparison between LED grow light and other systems

## Slide 8: Introduction
Conventional LED system for plant growth
  Users should control several conditions such as LED wavelength for plant
  Difficulty for automation
Conventional LED system
LED controller

## Slide 9: Introduction
IoT-based LED system for plant growth
  It can control a proper led wavelength automatically checking several sensors around the plant
  Also, plant information can be used for the automatic control
Sensors
Microcontroller
Grow lights
Monitor

## Slide 10: Components of system
Arduino mega 2560
Controller
Infrared distance
Cds light
Sensors
Temperature
Information display
Light
Grow light LED
LED controller
Mosfet
Telecommunication
Bluetooth
1st Proposed System

## Slide 11: Concept of system
IoT system concept based on microcontroller
  Calculating the distance between plant and led using Infrared sensor
  If distance is long, a PWM signal has large value
  If distance is short, a PWM signal has small value
The case that distance is long
1st Proposed System
The case that distance is short

## Slide 12: Proposed algorithm
Input target lux
  First, the proposed algorithm calculates several data for distance and light intensity
  Then, it generates database based on a LED model
,, : The distance between a target plant and LED
,, : The lux corresponding to ,,
Infrared sensor operation
Plant point extraction
Distance data calculation
PWM level generation
Input Target lux
Light emission
Linear Interpolation
1st Proposed System

## Slide 13: Proposed algorithm
Infrared sensor operation and plant point extraction
  The proposed system recognizes the position of the target plant
Infrared sensor operation
Plant point extraction
Distance data calculation
PWM level generation
Input Target lux
Light emission
Linear Interpolation
1st Proposed System

## Slide 14: Proposed algorithm
Distance calculation
  The PWM levels are computed based on the pre-determined target intensity(,, ) and the bilinear interpolation technique
,, : The distance between a target plant and LED
,, : The lux corresponding to ,,
Infrared sensor operation
Plant point extraction
Distance data calculation
PWM level generation
Input Target lux
Light emission
Linear Interpolation
1st Proposed System

## Slide 15: Proposed algorithm
Bilinear interpolation technique
  It is used to generate new pwm levels
  Using and depends on plant position (x)
: one of ,, is determined by plant position
: one of ,, is also determined by plant position
Bilinear interpolation for PWM
Y = Y)
Y : the interpolation function
Proposed system uses 8 bit for the intensity level
1st Proposed System

## Slide 16: Proposed algorithm
PWM level generation
  In this module, the proposed system calculates real LED intensity level, which is related with the power consumption
  For this, it converts a unit of lux to that of lumen, and calculates the LED power consumption which is based on a unit of lumens/watt
  Therefore, the proposed LED system can adaptively control the LED power consumption based on the position of a target plant
Infrared sensor operation
Plant point extraction
Distance data calculation
PWM level generation
Input Target lux
Light emission
Linear Interpolation
1st Proposed System

## Slide 17: Proposed algorithm
Light emission
PWM | Prototype
255 | 
180 | 
100 | 
30 | 
Infrared sensor operation
Plant point extraction
Distance data calculation
PWM level generation
Input Target lux
Light emission
Linear Interpolation
1st Proposed System

## Slide 18: Simulation environment
Target lux
  Test distances: 30, 50, 80, 100(cm)
  Several comparison between LED and plant is used for simulation in various height
  PWM is used to 8bit intensity level
Target lux (lux) | Height (cm) | PWM
100 | 30, 50, 80, 100 | 0~255 8bit intensity level
134 |  | 
200 |  | 
1st Proposed System

## Slide 19: Simulation environment
Watt from PWM
  Power is calculated by Look-up table (LUT)
  Typical luminous efficacy is 60 lm/W
Light Type | Typical luminous efficacy (lumens/watt)
Halogen lamp | 16 – 24 lm/W
Fluorescent lamp | 45 – 75 lm/W
Metal halide lamp | 75 – 100 lm/W
LED lamp | 30 – 90 lm/W
: luminous flux in lumens(lm)
: illuminance of lux
: surface area in light
: lumen / watt
1st Proposed System

## Slide 20: Simulation results
PWM level simulation
1st Proposed System

## Slide 21: Simulation results
PWM level simulation
1st Proposed System

## Slide 22: Simulation results
Target lux | Height | PWM | Watt
134 (default) | 100 | 255 | 16.333
 | 80 | 182.02 | 11.659
 | 50 | 72.55 | 4.647
 | 30 | 28.12 | 1.801
200 | 100 | 255 | 16.333
 | 80 | 196.31 | 12.574
 | 50 | 108.28 | 6.936
 | 30 | 41.98 | 2.689
100 | 100 | 190.30 | 12.189
 | 80 | 174.66 | 11.187
 | 50 | 54.14 | 3.468
 | 30 | 20.99 | 1.344
1st Proposed System

## Slide 23: Simulation results
1st Proposed System

## Slide 24: Motivation
For better plant cultivation environment, we suggest a new estimation algorithm using image segmentation
  It measures the health status of plants from their leaves
This algorithm is based on a chlorophyll (Chl) value
  Using image processing calculates Red and Blue values
  It substitute these values in Chl formula
[1] Mahmoodi, Mahmood, et al. "Chlorophyll Content Estimation Using Image Processing Technique.“WORLD APPLIED SCIENCES JOURNAL, pp.5~7, JANUARY 2013
2nd Proposed System

## Slide 25: Motivation
IoT system in home plant cultivation
  With IoT system that uses various web communication devices, we can check cultivation environment more efficiently
    Chlorophyll of the plant
    Growth
    Humidity
    …
  We proposed chlorophyll a new estimation algorithm using image segmentation-based plant recognition
Home plant cultivation system with IoT technologies
2nd Proposed System

## Slide 26: Pre-processing
To take high quality pictures of the plants, we controlled some conditions
  Luminance
  Same background conditions
  Distance
For the better accuracy of leaf detection, we classified leaves and the background of the pictures
  Leaf color : Green
  Background color : gray
2nd Proposed System

## Slide 27: Main processing
Color masking
Binarization of an image
Image restoration
Calculating chlorophyll
Image Input
Chlorophll Level
2nd Proposed System

## Slide 28: Main processing
Leaf extraction process
  Estimating typical size of a leaf in an input frame image
Color masking
Binarization of an image
Image restoration
Calculating chlorophyll
Image Input
Chlorophyll Level
2nd Proposed System

## Slide 29: Main processing
Leaf extraction process
Separating separate leaves and a background from the input image
  RGB color map was used
  It is important to select unique colors of the leaves
Color masking
Binarization of an image
Image restoration
Calculating chlorophyll
Image Input
Chlorophyll Level
2nd Proposed System

## Slide 30: Main processing
Leaf extraction process
After binarization, the image has zero and one values
  Leaf area: the area where the intensity are non-zeros
  To get a color image, multiplication is performed
    Original image.*binary Image (Vectorization)
Color masking
Binarization of an image
Image restoration
Calculating chlorophyll
Image Input
Chlorophyll Level
2nd Proposed System

## Slide 31: Main processing
Leaf extraction process
  For improving the accuracy of the calculation, background components are deleted
    Zero values are assigned in a background
  Calculating Chl with ‘R’ and ‘B’ in the training image
    Chl=R-B/R+B
Color masking
Binarization of an image
Image restoration
Calculating chlorophyll
Image Input
Chlorophyll Level
2nd Proposed System

## Slide 32: Main processing
Leaf extraction process
  Calculating Red and Blue values
  Comparing chlorophyll values from the image of leaves
  Classifying normal leaves and bad leaves
[1] Mahmoodi, Mahmood, et al. "Chlorophyll Content Estimation Using Image Processing Technique.“ WORLD APPLIED SCIENCES JOURNAL, pp.5~7, JANUARY 2013
Color masking
Binarization of an image
Image restoration
Calculating chlorophyll
Image Input
Chlorophyll Level
2nd Proposed System

## Slide 33: Simulation results
Original Image | Result Image
leaf_h_31 (RGB:0.0262 / H:0.0178) | 
Original Image | Result Image
leaf_hl_05 (RGB:0.0434 / H:0.0093) | 
2nd Proposed System

## Slide 34: Simulation results
Original Image | Result Image
leaf_h_33 (RGB:0.0220 / H:0.0152) | 
Original Image | Result Image
leaf_hl_19 (RGB:0.0433 / H:0.0105) | 
2nd Proposed System

## Slide 35: Simulation results
Chlorophyll value
2nd Proposed System

## Slide 36: Simulation results
Comparison between chlorophyll value normal case and bad case
Chlorophll value
Training information
2nd Proposed System

## Slide 37: Simulation results
There are difference between normal leaves and bad leaves
  Compared chlorophyll value(minimum,Maximum,mean)
  In this case, chlorophyll value of normal case is lower than the value of the other case
    Leaf with low chlorophyll values has high probability for normal case
 | Normal case | Bad case
Chl (Min.) | 0.0192 | 0.0229
Chl (Max.) | 0.0369 | 0.0621
Chl (Mean) | 0.0288 | 0.0337
2nd Proposed System

## Slide 38: Summary
We proposed a new intelligent LED control system for the plant cultivation
The proposed system..
  Detected the target plant position, and controlled the LED intensity according to the distance between the target plant and system
  Extracted the leaf portion using color mask and binarization and measured chlorophyll value using image processing
The simulation results…
  Shows the proposed system preserved the appropriate LED intensity for the target plant
  Reduced the power consumption significantly
  Normal leaf chlorophyll value is more lower than bad leaf chlorophyll