## Slide 1: Efficacy of a novel bactericide for elimination of biofilm in food processing facilities
Tong Zhao
Center for Food Safety
University of Georgia
For 3rd International Conference and Exhibition on Food Processing & technology

## Slide 2: Biofilm
Biofilms are single or multi layers of microorganisms embedded in their own extracellular polymeric substances (EPS) which associate with a solid surface
1. Initial attachment
2. Irreversible attachment
3. Microcolony
4. Maturation
5. Dispersion

## Slide 3: Biofilm
Predominant matrix for bacterial growth
~ 80% of all bacterial infections are biofilm-associated

## Slide 4: Problem
Cells in biofilms are more resistant to cleaning and disinfection processes than their planktonic counterparts
EPS
Slow growth
Gene expression

## Slide 5
Development of a novel bactericide
Effective, easy-to-use, cost-efficient, and environmentally friendly.
Levulinic acid and sodium dodecyl sulfate (SDS) were tested in combination at different concentrations and temperatures (8 or 82°C) either as liquid or foam for their killing effects on human pathogens formed as biofilms.

## Slide 6
Development of a novel bactericide
Effective, easy-to-use, cost-efficient, and environmentally friendly.
Levulinic acid and sodium dodecyl sulfate (SDS) were tested in combination at different concentrations and temperatures (8 or 82°C) either as liquid or foam for their killing effects on human pathogens formed as biofilms.

## Slide 7
Development of a novel bactericide
U. S. Patent and Trademark Office. U.S. patent number 8,722,123. Issue date: May 13, 2014. Antimicrobial Composition and Use as Food Treatment.
More than 10 papers regarding its application on dental, produce, poultry, and meat have been published.
Marked by HealthPro Brands.

## Slide 8: Results

## Slide 9
Chemical Inactivation of S. Enteritidis on biofilm as a liquid at 21°C
Coupon material | Chemical solution | Salmonella Enteritidis counts (log CFU/cm2) at minutes |  |  |  |  | 
 |  | 0 | 1 | 2 | 5 | 10 | 20
Stainless steel | PBS, pH 7.2 | 8.0 | 8.4 | 8.5 | 8.6 | 8.2 | 8.1
 | Acidified sodium chlorite (500 ppm), pH 2.8 | 7.5 | 5.9 | 5.7 | 5.4 | 6.2 | 6.0
 | 3% levulinic acid plus 2% SDS, pH 3.0 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7
Polyvinyl chloride | PBS, pH 7.2 | 8.8 | 9.0 | 8.1 | 8.8 | 8.0 | 8.3
 | Acidified sodium chlorite (500 ppm), pH 2.8 | 6.9 | 5.5 | 5.8 | 5.3 | 4.2 | 2.9
 | 3% levulinic acid plus 2% SDS, pH 3.0 | 2.3 | 1.7 | 2.0 | 2.2 | <0.7 | <0.7
Nitrile rubber | PBS, pH 7.2 | 7.8 | 8.0 | 8.5 | 7.7 | 7.9 | 7.7
 | Acidified sodium chlorite (500 ppm), pH 2.8 | 7.2 | 5.2 | 2.7 | 2.6 | 1.3 | <0.7
 | 3% levulinic acid plus 2% SDS, pH 3.0 | 4.1 | 1.7 | 1.7 | <0.7 | <0.7 | <0.7
Glass | PBS, pH 7.2 | 8.2 | 8.7 | 8.4 | 8.4 | 8.4 | 8.4
 | Acidified sodium chlorite (500 ppm), pH 2.8 | 6.8 | 3.3 | 0.7 | 0.7 | <0.7 | <0.7
 | 3% levulinic acid plus 2% SDS, pH 3.0 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7
Ultra-high molecular weight polyethylene | PBS, pH 7.2 | 8.4 | 8.4 | 8.6 | 8.4 | 8.4 | 8.4
 | Acidified sodium chlorite (500 ppm), pH 2.8 | 6.8 | 6.1 | 2.1 | 0.7 | <0.7 | <0.7
 | 3% levulinic acid plus 2% SDS, pH 3.0 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7

## Slide 10
Inactivation of S. Enteritidis on biofilm by 3% levulinic acid plus 2% SDS as a foam at 21°C
Coupon material | Chemical solution | Salmonella Enteritidis counts (log CFU/cm2) at minutes |  |  |  |  | 
 |  | 0 | 1 | 2 | 5 | 10 | 20
Stainless steel | PBS, pH 7.2 | 7.3 | 7.7 | 8.0 | 7.2 | 8.0 | 7.3
 | 3% levulinic acid plus 2% SDS, pH 2.8 | 8.3 | 6.7 | 6.8 | 4.0 | 2.3 | 2.0
Polyvinyl chloride | PBS, pH 7.2 | 8.0 | 8.3 | 8.2 | 8.6 | 8.2 | 8.6
 | 3% levulinic acid plus 2% SDS, pH 2.8 | 5.8 | 4.9 | 3.1 | 3.0 | 3.2 | 1.0
Nitrile rubber | PBS, pH 7.2 | 7.4 | 7.6 | 7.6 | 7.5 | 7.4 | 7.2
 | 3% levulinic acid plus 2% SDS, pH 2.8 | 7.1 | 4.1 | 3.5 | 3.3 | 2.4 | 1.7
Glass | PBS, pH 7.2 | 8.0 | 8.5 | 7.7 | 7.9 | 7.8 | 7.9
 | 3% levulinic acid plus 2% SDS, pH 2.8 | 4.9 | 4.4 | 3.3 | 3.5 | 1.7 | 1.7
Ultra-high molecular weight polyethylene | PBS, pH 7.2 | 6.9 | 6.9 | 6.7 | 6.4 | 6.7 | 6.3
 | 3% levulinic acid plus 2% SDS, pH 2.8 | 5.4 | 4.6 | 2.9 | 2.3 | 1.7 | 1.7

## Slide 12
Chart: Log CFU/blade
| Water | Quat sanitizer (150 ppm) | 0.5%LA+0.05%SDS | 1%LA+0.1%SDS | 2%LA+0.5%SDS | 0.5%LA+0.05%SDS(Foam) | 1%LA+0.1%SDS(Foam) | 2%LA+0.5%SDS(Foam) | Water | Quat sanitizer (150 ppm) | 0.5%LA+0.05%SDS | 1%LA+0.1%SDS | 2%LA+0.5%SDS | 0.5%LA+0.05%SDS(Foam) | 1%LA+0.1%SDS(Foam) | 2%LA+0.5%SDS(Foam) | Water | Quat sanitizer (150 ppm) | 0.5%LA+0.05%SDS | 1%LA+0.1%SDS | 2%LA+0.5%SDS | 0.5%LA+0.05%SDS(Foam) | 1%LA+0.1%SDS(Foam) | 2%LA+0.5%SDS(Foam) | L. monocytogenes | S. Typhimurium | E. coli O157:H7
0 min | 8.4 | 4.4 | 5.4 | 3.2 | 1.5 | 1.4 | 1.4 | 0 | 6.6 | 5.1 | 4.6 | 3.9 | 0 | 1.4 | 1.4 | 1.4 | 6.7 | 6.1 | 6.2 | 4.3 | 0 | 2.4 | 3.1 | 0
1 min | 8.1 | 1.4 | 4.5 | 2.3 | 0 | 0 | 0 | 0 | 6.7 | 4.8 | 3.2 | 1.5 | 0 | 0 | 0 | 0 | 6.4 | 4.7 | 6.1 | 3.8 | 1.4 | 1.4 | 0 | 0
2 min | 7.9 | 0 | 3.6 | 1.4 | 0 | 1.4 | 0 | 0 | 5.6 | 2 | 2.8 | 1.4 | 0 | 0 | 0 | 0 | 5.5 | 3.8 | 4.9 | 2.4 | 0 | 0 | 0 | 0
3 min | 7.3 | 0 | 2.4 | 0 | 0 | 0 | 0 | 0 | 5.3 | 1.8 | 1.7 | 0 | 0 | 0 | 0 | 0 | 6.2 | 2.1 | 4.5 | 1.9 | 0 | 0 | 0 | 0
5 min | 7.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.9 | 0 | 3.1 | 1.4 | 1.4 | 0 | 0 | 0
10 min | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.3 | 0 | 1.4 | 0 | 0 | 0 | 0 | 0
20 min | 5.6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.9 | 0 | 0 | 0 | 0 | 0 | 0 | 0
30 min | 6.8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.9 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 14
Before chemical treatment
The Salmonella isolation rate was 19% (19/100).
The fecal coliform population averaged 6.8 CFU/25 cm2 log (ranged from 3 to 9.3 log CFU/25 cm2).
The total aerobic bacteria count averaged 7.9 log CFU/25 cm2 (ranged from 5.7 to 9.9 log CFU/25 cm2).
After treatment with 3% levulinic acid plus 2% SDS as a foam
The Salmonella isolation rate was 1% (1/100).
The fecal coliform population averaged 1.15 log CFU/25 cm2 (ranged from 0.6 to 3.1 log CFU/25 cm2), a 5.6 log CFU/25 cm2 reduction.
The aerobic bacteria count averaged 4.8 log CFU/cm2 (ranged from 1.6 to 7.5 log CFU/25 cm2), a 3.2 log reduction.

## Slide 15
Biofilm Growth
10-min Heat Treatment
10-min Sanitizer Treatment
72 h
100% RH
21°C
60, 80, and 100°C
QAC, 150 ppm quaternary ammonium-based sanitizer;
LA, 3% lactic acid;
SHC, 100 ppm sodium hypochlorite;
HP, 2% hydrogen peroxide;
LVA, 3% levulinic acid;
SDS, 2% sodium dodecyl sulfate
0.5% LVA + 0.05% SDS
1% LVA + 0.1% SDS
3% LVA + 2% SDS
and / or

## Slide 16: Acid Shock
Bacteria counts of selective agar plates and TSA of 72-h biofilms of L. monocytogenes, S. Typhimurium, and STEC formed on stainless steel after a 10-min treatment with 3% lactic acid (pH 2.2) or 3% levulinic acid (pH 2.7).

## Slide 17: 10-min Heat Treatment
Chart: Temperature (°C)
| 21 | 60 | 80 | 100
L. monocytogenes | 8.6294 | 7.6937 | 7.6453 | 6.9096
S. Typhimurium | 8.9358 | 8.3266 | 7.5267 | 7.3743
STEC | 9.2301 | 8.4648 | 7.4726 | 6.564
*
Inactivation of 72-h biofilms of L. monocytogenes, S. Typhimurium, and STEC formed on stainless steel after receiving 10-min heat treatment at 21, 60, 80 or 100ºC.
*
*
*
*
*
*
*

## Slide 18: 80°C + Sanitizer Treatment
Chart: Sanitizers
| Water | QAC | LA | SHC | HP
L. monocytogenes | 7.6 | 0 | 0 | 3.7 | 5.1
S. Typhimurium | 7.5 | 6.6 | 0 | 2 | 4.9
STEC | 7.5 | 6.2 | 0 | 7.2 | 7.1
Inactivation of 72-h biofilms of L. monocytogenes, S. Typhimurium, and STEC formed on stainless steel after receiving a 10-min 80°C treatment and a subsequent 10-min sanitizer treatment.
*
* * *
*
*
*
*

## Slide 19: 10-min Sanitizer Treatment
Chart: Sanitizers
| Water | QAC | LA | SHC | HP | LVA | SDS | 0.5% LVA + 0.05% SDS | 1% LVA + 0.1% SDS | 3% LVA + 2% SDS
L. monocytogenes | 8.6294 | 4.1526 | 2.1326 | 7.003 | 8.3366 | 8.2612 | 7.4217 | 1.8 | 0 | 0
S. Typhimurium | 8.9358 | 8.0362 | 0 | 3.1516 | 6.2665 | 4.3715 | 8.6385 | 5.5159 | 2.8157 | 0
STEC | 9.2301 | 7.4325 | 0 | 7.5581 | 7.5132 | 6.4353 | 8.8224 | 6.9186 | 5.9267 | 0
Inactivation of 72-h biofilms of L. monocytogenes, S. Typhimurium, and STEC formed on stainless steel after receiving a 10-min sanitizer treatment.
*
* *
*
* * *
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*

## Slide 20
Representative images made by TEM of biofilms formed by Listeria monocytogenes (A, B), Salmonella (C, D), and STEC (E, F) after a 10-min treatment with water (control, A, C, E), and 0.5% levulinic acid + 0.05% SDS (B, D, F).

## Slide 21
Representative images made by SEM of biofilms formed by Salmonella after a 10-min treatment with water (control, A), 0.5% levulinic acid + 0.05% SDS (B), 1% levulinic acid + 0.5% SDS (C), and 3% levulinic acid + 2% SDS (D).

## Slide 22
Conclusions
All foodborne pathogens as tested, including E. coli O157:H7, Salmonella, L. monocytogenes have the potential to form the biofilms on the surface of materials that commonly used in the processing facilities.
Levulinic acid-based sanitizer either in liquid or in foam has strong ability to remove or eliminate the biofilms.

## Slide 23
Michael P. Doyle, Dong Chen, Yen-con Hung, Ping Zhao, University of Georgia; and Juan F. DeVillena, Wayne Farms LLC, for his technical assistance.
Acknowledgements
This study was supported by grants from the Center for Food Safety, University of Georgia; the National Institute of Food and Agriculture, U. S. Department of Agriculture; and the State of Georgia’s Traditional Industries Program for Food Processing.