## Slide 1
Recycling practices and material flow analysis of mercury-containing fluorescent lamps in Korea
Yong-Chul Jang
Chungnam National University, Daejeon, Korea

## Slide 2
1. Intro
2. EPR System of Fluorescent Lamps
3. MFA of Fluorescent Lamps
4. Current issues of Spent Fluorescent Lamps management
5. Future direction
CONTENTS

## Slide 3
1.
Introduction

## Slide 4
Intro.
Intro.
Chart: 
| 2011 | 2012 | 2016 | 2020
Total | 3537 | 3663 | 4283 | 5112
Incandescent | 867 | 758 | 229 | 111
Halogen | 607 | 640 | 612 | 329
HID | 48 | 48 | 39 | 24
LFL | 661 | 682 | 645 | 511
CFL | 1224 | 1251 | 1170 | 852
LED | 130 | 283 | 1587 | 3285
4 billion pcs/ year
World General Lighting Market
Source : McKinsey, 2012
(Linear Flourescent lamp)
(Compact Flourescent lamp)
(Unit : million pcs)

## Slide 5
Intro.
Quantities of Mercury in Lamps | 
Type of Lamps | Avg. Amount
CFL (Compact Fluorescent Lamps) | 1-25 mg
U-Tubes FL | 3-12 mg
Fluomeric Lamps | 2 mg
LFL (Linear Flourescent Lamps) | 10-50 mg
Mercury Reduced LFL | 3-12 mg
Mercury Vapour Lamps | 25-225 mg
Metal Halide Lamps | 25-225 mg
Sodium Vapour Lamps | 20-145 mg
Fluorescent lamps
Source : Guide to Recycling Mercury- Containg Lamps, Northewest Territories Environment and Natural Resource

## Slide 6
Intro.
Hg
Mercury and Minamata Convention
Elemental and inorganic
: Exposed directly through occupation
Organic (e.g., Methylmercury)
: Exposed indirectly through diet
(Bioaccumulation)
Mercury is a chemical of global concern owing to its long-range atmospheric transport, its persistence in the environment, its ability to bioaccumulate in ecosystem and its significant negative effects on human health and the environment
Recently, Minamata Convention was agreed to ban on new mercury mines, the phase-out of existing ones, control measure on air emissions in 2013.
Notes: Mercury exists in various forms: elemental and inorganic (to which people may be exposed through their occupation); and organic (e.g., methylmercury, to which people may be exposed through their diet). These forms of mercury differ in their degree of toxicity and in their effects on the nervous, digestive and immune systems, and on lungs, kidneys, skin and eyes.

## Slide 7
* Controlling the anthropogenic releases of mercury throughout its lifecycle has been a key factor in shaping the obligations under the convention
MINAMATA CONVENTION ON MERCURY

## Slide 8
MINAMATA CONVENTION ON MERCURY

## Slide 9
2.
EPR System of FL in Korea

## Slide 10
EPR : Extended Producer Responsibility
Production
Sale
Cosumption
Discard
Recycling
Past
Present
EPR system is an environmental protection strategy
to decrease total environmental impact of a product,
by making the producer of the product responsible
for the entire life-cycle of the product and especially for the take-back, recycling and final disposal.
Responsibility
Notes: Came into force

## Slide 11
1
Linear shape (LFL) | Round shape (FCL) | U-tube shape (FPL) | Contains inverter (CFL)
Recycling targets of fluorescent lamp in Korea EPR system
In Korea, there are 4 recycling targets of FL in EPR system .
Each year, recycling target rate of used lamps is set and should be achived.

## Slide 12
1w
Municipalities (Collectors)
(Fund support)
(Entrust)
MOE
(Ministery of Environment)
Korea Environment Corperation
Korea Light Recycling Cooperative
Recyclers
Producers
(Monitoring)
(Target rate)
(Report result)
(Guidance)
(Report recycling responsibility and statistics)
(Share of expenses)
(Recylcing)
Flow of product
Flow of waste
Financial Flow
Report System
EPR system of fluorescent lamp in Korea
(Source : MOE, EPR 시행 10년 성과평가 및 발전방향 연구, 2010)
Retailers
Consumers
(Industiral)
Consumers
(Households)
(Collection & Recycling)
(Collection & Disposal Fee)

## Slide 13
Collection points of fluorescent lamp in Korea

## Slide 14
Collection points of fluorescent lamp in Korea

## Slide 15
(Source : SBS News 2014. 10. 30)
Mercury lamps waiting for disposal at collection site in Korea
Improper disposal of mercury lamps causes a concern in community by media in 2014
Transfer station of fluorescent lamp in local government

## Slide 16
FL recycling facilities in Korea
 | Facility A | Facility B | Facility C
Equipment | Straight type 1 line other type 3 line HID type 1 line | Straight& other type 1 line | Straight& other type 1 line
Treatment Capacity | Straight type : 5,000 unit/h HID type : 2,500 unit/h | Straight & other type : 5,000 unit/h | Straight&other type : 5,000 unit/h
Treatment Technology | Modified MRT (Sweden) | Modified Herbon (Germany) | Modified Herbon (Germany)
There are 3 FL recycling facilities operated in Korea
3 more FL recycling facilities are planned to operate in 2015
Current recycling facility
Future recycling facility
A
B
C

## Slide 17
General SFL recycling process in Korea
Linear Lamp Input
Cutting base
Drum sorting
Glass sorting
Mixed metal sorting
Glass heating
Glass cooling
Fine metal sorting
Other type Lamp Input
Shredder
Drum sorter
Powder heating
Powder cooling
Powder outlet
Mercury distillator
Mercury recovery
Base outlet
Source : Korea Lighting Recycling Corporation

## Slide 18
(Unit : 1,000 unit)
Chart: Fluorescent Lamp
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Lamp manufacutred | 118836 | 138586 | 134148 | 130750 | 120268 | 116233 | 126756 | 148289 | 164438 | 149452
SFL Recycled | 17369 | 26398 | 29546 | 27282 | 30711 | 32655 | 35269 | 37952 | 49196 | 42707
Recycling target | 17469 | 26192 | 26390 | 29439 | 27802 | 27896 | 33083 | 42262 | 49331 | 49020
Statistic Data of FL Management in Korea
  SFL Recycling target has been continuously increasing since 2004
  SFL recycling rate is still low compared to the amount in the market.

## Slide 19
3.
MFA of lamps in Korea

## Slide 20
MFA (Material Flow Analysis) is an analytical method
of quantifying flows and stocks of materials or substances
in a well-defined system.
It is based on the law of mass conservation.
Defining system boundary
Selection of target material & Setting system boundary
Investigation of general material flow in each life-cycle stage
Setting data range & collection of data
Calculation & Verification of data
Result analysis
Drawing material flow diagram
<MFA Process >
MFA
MFA Definition
Quantifying flow and stocks

## Slide 21
MFA
Discharging lamp
Filament lamp
FL
Low pressure
discharge lamp
High pressure
discharge lamp
Special FL
Target of
MFA subject of
Fluorescent lamps
Defining system
boundary
Resource
Extraction
Product Manufacture
Product Use
Waste Collection
Waste Recycling
Waste Disposal
System boundary : Household sector
Time boundary :
1 year (2013)

## Slide 22
Data collection : Field & Literature survey
▶ Data of disposal stage was not sufficent
whereas data of production stage
and recycling stage is avalilable to collect
▶ Stages difficult to collect data were estimated
through field survey, literature investigation,
expert adivce
▶ When data estimated through mass balance
had uncertainty, they were modified and
complemented with consideration of
material flow interrelationship
MFA
Life cycle | Data | Data collection method |  | 
 |  | Statistics | Literature survey | Field survey & advice
Import | FL Import | ○ |  | 
Production | Shipment | ○ |  | 
 | FL Production·Domestic market·Export | ○ |  | 
 | LED market |  | ○ | 
Use | Household use |  | ○ | 
 | Industrial use |  | ○ | 
 | Stock |  |  | ○
Collection | Municipality collection | ○ |  | 
 | Collection by entrustment | ○ |  | 
 | Dumping |  |  | ○
Recycling | Input of RC | ○ |  | 
 | Output of RC | ○ |  | 
Disposal | Incineration |  | ○ | 
 | Landfill |  | ○ | 
Data collection & Sources for MFA of FL

## Slide 23
  Shipment = Domestic Market + Export
  Total Output = Domestic Market + Import
 | Total Output | Import | Production | Shipment | Stock | Domestic Market | Export
2013 | 149,453 | 107,521 | 45,958 | 45,572 | 4,129 | 41,932 | 3,640
*Source : Statistics Korea, Korea Environment Corporation
MFA
Output data
collection
Unit : 1,000 unit

## Slide 24
MFA
Source | Product Life time (Years)
Korean Standards & Certification | 2.47
Green Purchasing Network | 2.81
OSRAM | 5.21
Average | 3.5
Product
Life Time
Take-back to store(0.3%)
Disposal (Broken) in MSW bags (3.2%)
Disposal (Unbroken) in MSW bags (7%)
others(2.7%)
Collection box (83.8%)
Survey
Result
In Daejeon city
(Household)
Disposal data
Estimation

## Slide 25
MFA
 | Disposal in envelope (Not broken) | Disposal in envelope (Broken) | Collection box | Take-back to the store | Etc. | Total
2013 | 3,209 | 1,406 | 36,832 | 132 | 1,187 | 42,766
Unit : 1,000 unit
  The number of SFL by disposal shape was estiamted based on citizen survey
  Stock = The number of disposal × replacement period = around 149 million unit
(Household)
Disposal data
Estimation
2015
2014
2013
2012
2011
Produce 1000 unit/ year, Product Life time : 4 years
Disposal
1,000 FL
1,000 FL
1,000 FL
1,000 FL
1,000 FL
Example-Lifetime

## Slide 26
MFA
(Household)
Recycling Data
collection
 | Straight FL | Compact FL | Contains inverter | Average | % Ratio
Glass | 134.60 | 89.60 | 54.90 | 103.43 | 80.2%
Fluorescent material | 2.80 | 0.90 | 0.05 | 1.64 | 1.3%
Metal | 1.45 | 1.20 | 0.60 | 1.18 | 0.9%
Aluminum | 2.25 | - | 3.30 | 1.95 | 1.5%
Glue | 9.10 | 2.90 | 90 | 7.25 | 5.6%
Plastic | - | 9.80 | 18.90 | 7.18 | 5.6%
Inverter | - | - | 25.40 | 6.35 | 4.9%
Sum | 150 | 104 | 111 | 128.96 | 100.0%
 | % Ratio | Recycling amount | Actual result*
Glass | 80.2% | 4,447 | 4,015
Plastic | 5.6% | 308 | 372
Aluminum | 2.4% | 134 | 170
Powder | 11.8% | 655 | 469
Sum | 100.0% | 5,545 | 5,025
SFL componets by product type
SFL recycling amount by componets
Unit : g, %
Unit : g, %
* Source : Korea Environment Corporation
* Source : Development of valuable material recovery technology of Waste lighting equipment, 2011

## Slide 27
MFA
Collection box
36,832
Retailers
132
Collection by city
36,964
Recycling
36,964
Production
45,958
Domestic demands
41,932
Import
107,521
Shipment
45,572
Use in home
140,226
Disposal bag with broken 1,406
landfills
2,321
Incineration
3,481
Export
3,640
Sold to industrial sector
106,687
glass
4,447 ton
Others
1,187
Disposal bag
3,209
plastic
308 ton
Al
134 ton
particulate
665 ton
Total
Domestic demands
149,453
Storage
386
Disopsal
Recycling
5,743
Solid waste
Collectors
5,743
Generation from home
42,766
Unit | 1,000
Time | 2013
Hidden flow

## Slide 28
4.
Current issues of lamps
Management in Korea

## Slide 29
If SFLs are discharged in broken shape, mercury vapor will be exposed to the surrounding environment
Mixed waste in SFL collection box caused additional cost and labor force on segregation and collection stage
Disposal
Stage

## Slide 30
Collection
Stage
Current issues of SFL Management in Korea
Household
Industrial
74% Recycling rate
 | Generation | Recylcing
Household | 50,000 | 36,964
Industrial | 100,000 | 5,793
Unit : 1,000 unit
6% Recycling rate
Recycling rate from industrial sectors is relatively low compared to household sectors

## Slide 31
Transportation
Stage
Transportation cost is high because of long distance from municipality to recycling facility
Cumulated SFL have been issued in capital region because of high transportation cost and long distance

## Slide 32
Recycling
Stage
Mercury concentration in recovery materials was higher than standard level(0.005mg/L)
There is no regulation on mercury concentration in recovery materials of SFL
Mercury concentration in workplace atmosphere was higher than OSHA PEL standard in US (lower than 0.1 mg/m3 every moments)
Management of elemental mercury storage and transportation was incomplete
Introdunced recycling technology from abroad was modified or some facilities are eliminated for convenience

## Slide 33
5.
Future Directions
and summary

## Slide 34
Disposal
stage
Collection
stage
Recycling
stage
Establishment of more effective collection system for SFL of industrial sector
Installation more collection box for residents availablity
More strict recycling guidlines
Expension of EPR subjectlamp containing mercury
Establishment of take-back system for retailers
Establishment of safe recovery and recycling foundation for mercury
Addition of LED lamp to the EPR system
Management of SFL of industrial sector to the industrial waste registration system
Development of recyling technology for LED lamp
Short term
Mid term
Long term
Future Direction
Remediation direction of SFL management

## Slide 35
Current states and anticipation of the world LED industry
LED lamp market is anticipated to sharply grow with decreasing LED price and impelmentation of carbon emission trading system
Life-time of LED lamp (30,000-50,000 hours) is 3~4 times longer than that of fluorescent lamp (8,000 hours)
(Source : Meritz Investment Bank Research Center)
(Trillion won)
2011
2012
2013
2014
2015
2016
9.2
15.5
20.3
27.4
34.6
42.9
Replacement
New installation
Scale of entire lamp market
123
127
131
134
138
143
147
160
170
2
4
6
9
15
21
28
52
75
2
5
8
12
21
30
41
83
128
Scale of LED lamp market
Market share of LED
09
10
11
12
13
14
15
18
20
(%, triilion won)
(Year)
Future Direction

## Slide 36
Even though LED lamp doesn’t contain Mercury, it has hazardous and valuable materials such as antimony, copper, lead, nickel, and zinc
In some crushed specimen, leaching test results showed some concerns of leaching due to several hazardous materials found in LED lamp (Lim et al., 2010)
Some EU country have already been implementing LED recycling duty with fluorescent lamp
It may be required to add LED lamp to the EPR system and establish appropriate management directives
Future Direction
LED lamp

## Slide 37: Thank you for your attention !

## Slide 38
Q&A